## Slide 1
SakhyaPath
Evidence backed CCTV intelligence for Gujarat
HYBRID ARCHITECTURE · LOCAL PROTOTYPE
Notes: Conceptual illustration generated for this deck; it is not a Government feed. Project status and scope: README.md and docs/SUBMISSION_READINESS.md.

## Slide 2
PROBLEM AND BRIEF
The challenge
SAKHYAPATH · GUJARAT CCTV HACKATHON
02
26 departments
Existing CCTV spans different vendors, formats and locations.
Mandatory foundation
A common camera registry and GIS view must precede selective analytics and cross camera search.
The live evaluation calls for roughly 50 heterogeneous feeds, vehicle history, watchlist alerts and a credible path to about 80,000 cameras.
Notes: Source: hackathon_source_index/README.md, especially background, Model 1, technical evaluation, and statewide scale plan.

## Slide 3
PROTOTYPE
What we built locally
SAKHYAPATH · GUJARAT CCTV HACKATHON
03
01
Camera grid
Registry, map, Sentinel catalogue adapter, owned RTSP/HLS capture and controlled preview.
02
Evidence trail
Plate reads, crops, watchlist alerts, historical search, journey map and reviewer corrections.
03
Adaptive pursuit
Measured analysis budget, camera ranking and a ledger that records what was viewed, missed or unavailable.
Notes: Source: README.md; docs/MODULE1_RUNBOOK.md; docs/MODULE2_RUNBOOK.md; docs/MODULE3_RUNBOOK.md; docs/MODULE4_RUNBOOK.md. These are locally implemented features.

## Slide 4
USER WORKFLOW
A case follows the evidence
SAKHYAPATH · GUJARAT CCTV HACKATHON
04
1 Register a vehicle of interest
2 Read authorised camera frames and save source timing
3 Confirm plate evidence and compare with the watchlist
4 Show the journey, uncertainty and coverage gaps
A human reviewer can correct detections and export the case report.
Notes: Source: SakhyaPath_technical_blueprint.md; docs/MODULE3_RUNBOOK.md; docs/MODULE4_RUNBOOK.md. Evidence and inference are distinct in the UI and reports.

## Slide 5
DISTINCTIVE APPROACH
Coverage is part of the answer
SAKHYAPATH · GUJARAT CCTV HACKATHON
05
The ledger records:
Seen and analysed
Available but skipped
Temporarily unavailable
Unknown or unverified
A missing sighting is not proof that a vehicle was absent.
Notes: Conceptual map image generated for this deck, not real footage or GIS data. Source of product logic: docs/MODULE4_RUNBOOK.md and docs/MODULE4_HLD.md.

## Slide 6
BENCHMARK
A measured local baseline
SAKHYAPATH · GUJARAT CCTV HACKATHON
06
2
owned replay feeds
249
analysed frames in 20.634 seconds
12.067 fps observed across both feeds
Planning budget: 8.447 fps with a 30% reserve. This is a local, two feed test; it is not a statewide capacity result.
Notes: Source: output/benchmarks and docs/SUBMISSION_READINESS.md. Local owned replay test, not Sentinel or Indian-road holdout footage.

## Slide 7
EXPERIMENT
Adaptive sampling has limits
SAKHYAPATH · GUJARAT CCTV HACKATHON
07
Expected branch
The adaptive allocator found more target observations under the same sample budget.
Surprise branch
Uniform sampling found the unpredicted route more often in the controlled test.
Next validation: reset recorded routes, common clock checks and held out ground truth from multiple cameras.
Notes: Source: docs/MODULE4_RUNBOOK.md and output/benchmarks. The official sample comparison is controlled and cannot establish field performance. scripts/compare_recorded_sampling.py is ready for permission-cleared footage.

## Slide 8
SCALE PLAN
Path to Government deployment
SAKHYAPATH · GUJARAT CCTV HACKATHON
08
01
Authorised pilot
Prove catalogue sync, mixed codecs, source timestamps, 50 feed onboarding and timestamped detections.
02
Regional services
Add PostgreSQL/PostGIS, durable events, regional capture workers and encrypted evidence.
03
Statewide expansion
Size active analysis, bandwidth, retention and recovery from measured pilot data.
Notes: Source: docs/PRODUCTION_GATE.md; docs/MODULE4_HLD.md; output/benchmarks/capacity_50_assumptions.json; output/benchmarks/capacity_80000_assumptions.json. These are phases and assumptions, not completed deployments.

## Slide 9
SUBMISSION GATES
Private live test still needed
SAKHYAPATH · GUJARAT CCTV HACKATHON
09
Sentinel access
Approve the account and provide the private catalogue origin and authentication.
Organiser live test
Evaluators supply private feeds and target vehicles. No Government footage leaves their sandbox.
Approved evidence
Show timed detections and a derived report live. Save media only when expressly permitted.
Reproducible links
Publish the presentation, HLD and code. Follow the organiser’s rule for any live-test recording.
Notes: Source: user-supplied Sentinel integration reference; docs/SENTINEL_OFFLINE_READINESS.md; docs/SUBMISSION_READINESS.md. Government footage stays private with the organisers. Local protocol tests do not prove Government integration or Indian-road model accuracy.